## Slide 1: Space Debris Deorbiter California State University, Los Angeles Department of Mechanical Engineering May 6, 2021
Edgar Herrera
Sponsor
Ted Nye
Advisor
James Cook
Maya Horii
Jasmine Lopez-Gutierrez
Gustavo Munoz
Victor Ramirez
Emily Silva

## Slide 2: Agenda
Introduction/Background Emily
System Engineering/Overview Maya
Debris Capture System James
Spacecraft Victor
Deorbit System Gustavo
Propulsion System Jasmine
Conclusion Emily

## Slide 3: Environment in space
Illustration of Small Satellite Configurations
Illustration of Debris
Sources: Live Science and talk Satellite

## Slide 4: Over 20,000 pieces of debris in low Earth orbit (LEO)
Illustration of Debris Orbits
Number of Objects in LEO Larger Than 10cm
1960
1970
1980
1990
2000
2010
2020
Year
5000
10000
15000
20000
Number of Objects
0
Iridium-Cosmos Collision
Anti-Satellite Test
Sources: Stuff in Space and NASA
Notes: NASA LEGEND Model: https://orbitaldebris.jsc.nasa.gov/modeling/legend.html

## Slide 5: Objective
To develop a small satellite (SmallSat) that is capable of capturing and deorbiting debris from low Earth orbit

## Slide 6: Requirements were met except for one
Requirement | Value | Capability | Method of Verification
Size of SmallSat | ≤ 60.1 cm diameter, 594.4 cm height | 20cm*20cm*30cm | Design and Analysis
Mass of SmallSat | ≤ 257 kg | 22.8 kg | Analysis
Time to Deorbit | ≤ 25 years | ≤ 16.2 years (0° to 80° inclination) | Analysis
Power | 48 Watts | 97.3 Watts | Design and Analysis
Weight of Debris | 1 kg ≤ M ≤ 12kg | 1 kg | Analysis
Size of Debris | 10 cm ≤ Size ≤ 60cm | 10 cm * 10 cm * 10 cm | Analysis
Vacuum to Sustain | 10^-6 Torr | Complies | Analysis
Temperature Range | -30°C ≤ T ≤ 30 °C | Complies | Analysis
Launch Load | 15 g in each orthagonal axis, non-simultaneously | Complies | Analysis
Number of Debris | ≥ 2 pieces | 1 piece | Design and Analysis
Notes: Am I supposed to leave the ESPA class requirements? Do I add derived requirements
https://www.unoosa.org/documents/pdf/spacelaw/sd/IADC-2002-01-IADC-Space_Debris-Guidelines-Revision1.pdf

## Slide 7: Agenda
Introduction/Background Emily
System Engineering/Overview Maya
Debris Capture System James
Spacecraft Victor
Deorbit System Gustavo
Propulsion System Jasmine
Conclusion Emily

## Slide 8: Most Debris in 700-1000km Altitude, 30-90° Inclinations
Debris Distribution by Altitude
(T. Schildknecht, January 2007)
2000
End of LEO
Altitude (km)
Inclination (°)
Altitude (km)
Inclination (°)
Debris Distribution by Orbit Inclination
(National Academy Press, 1995) (D. Mehrholz et. al, February 2002)
Notes: Mass and AMR distributions also in 11-20-2020, inclinations ones w links from 10-30-2020
T. Schildknecht, “Optical surveys for space debris,” The Astronomy and Astrophysics Review, vol 14, pp. 41-111, January 2007.
[4] “Orbital Debris: A Technical Assessment,” National Academy Press, Washington D.C., 1995.
[5] D. Mehrholz et. al, “Detecting, Tracking and Imaging Space Debris,” EESA Bulletin, vol 109, pp. 128-134, February 2002.

## Slide 9: Mission Overview
Ground Communications Receiver
Debris
Debris Capture Satellite

## Slide 10: Concept of Operations
Drop off satellite near debris
Approach and align with the debris
Use sensors to analyze debris
Deploy weighted boom
Attempt capture and determine success
Deploy deorbit method, determine success
Notes: https://collection.maas.museum/object/141107
Debris image

## Slide 11: We Can Capture Debris at Collision Speeds of 11.9mph
Impact at 5.3 m/s, Offset 20cm in Y-Dir
CubeSat
10m Boom
1kg Weight
CubeSat with Boom Diagram
Adding a weighted boom allows for collision speeds up to 5.3 m/s (11.9 mph):

## Slide 12: Agenda
Introduction/Background Emily
System Engineering/Overview Maya
Debris Capture System James
Spacecraft Victor
Deorbit System Gustavo
Propulsion System Jasmine
Conclusion Emily

## Slide 13: Spacecraft Deployed
12U Structure
Delta V Thruster
Antenna System
340mm
214 mm
214 mm
Debris Capture Mechanism
Stabilizing Boom

## Slide 14: Spacecraft Deployed From ISIS Dispenser
Spacecraft uses an ISIS 12U/16U Dispenser to deploy into orbit from launch vehicle

## Slide 15: Spacecraft Interior
Electrodynamic Tether (Undeployed)
Propulsion System / Fuel Tank
Power/ Battery System
Communication/Data Handling System

## Slide 16: Mass and Power Meet Requirements

## Slide 17: Agenda
Introduction/Background Emily
System Engineering/Overview Maya
Debris Capture System James
Spacecraft Victor
Deorbit System Gustavo
Propulsion System Jasmine
Conclusion Emily

## Slide 18: Capture Mechanism – Rigid Net (Catcher's Mitt)
Design ​ | Stowed Volume | Weight | Capture Object Size | Maneuverability | Power​ | Complexity (1-5) | Technology Readiness Lvl.​
Rigid Net | 2U​ | <1kg | 16U | Can be rotated if still attached to cubesat | .05-1 W​ | 2 | 4
Net | 1.5U | <6kg​ | 12U | Not maneuverable once released from CubeSat | 15W​ | 1 | 8
Boom w/ Adhesive | 2.5U | <2kg​ | 6U | Moderate Maneuverability | 20W​ | 1 | 4
Harpoon | 1U | <2kg​ | 3U | Not maneuverable once released from CubeSat if cable is used | 15W | 2 | 7
Cage | 9U​ | <10kg | 3U-6U | Highly maneuverable | 60W​ | 4 | 2
Boom w/ Grabber Claw | 6U (est.)​ | <5kg​ | 3U-6U | Less maneuverable | 40W+​ | 1 | 3

## Slide 19: Capture Mechanism – Deployed State
50cm
40cm
Capture mechanism top view
Carbon fiber stems released on deployment to keep debris in net
4 individual net sections
4 sets of 3-tiered Carbon Fiber arms curved to maximize capture volume
Arms set to open position until debris is inside net

## Slide 20: Capture Mechanism – Stowed State
Stowed capture mechanism Isometric view w/ top made transparent
When SmallSat is released from ISIS platform the arms undergo a passive spring deployment.
Arms and stems folded within each other. Arms are spring loaded and held down by platform door.
0.2cm
20 cm
Section of net will fold into storage structure with arms

## Slide 21: Capture Mechanism – Deployment using Springs & Hinges
Necessary torque was calculated to find spring constant. It was concluded to use same constant for all springs.
Spring deployment modeled in Solidworks at each joint. Mass of net was factored into calculations
Est. Force(N) | Min. Torque(N-m) | Est. Torque (N-m) | Spring Constant (N-m/deg) | Preload (N)
1.8 | 0.36 | 0.72 | 0.00514 | 0.9
Example of "door" hinge set in closed position.

## Slide 22: Agenda
Introduction/Background Emily
System Engineering/Overview Maya
Debris Capture System James
Spacecraft Victor
Deorbit System Gustavo
Propulsion System Jasmine
Conclusion Emily

## Slide 23: Electrodynamic Tether was Chosen
 | Deorbit Time | Size | Mass | Power | Active/Passive | Spacecraft Complexity (1-5) | Risk of Failure (1-5) | TRL
Electrodynamic Tether | 25 years | 0.6U | 0.8 kg | 0.9W – 25.2 W | Passive | 2 | 3 | 7
Drag Sails | 25 years | 2U (25m^2) | 10 kg (est.) | N/A | Passive | 3 | 2 | 9
Solar Sails | 8 months | ~1U (10m^2) | 4.2 kg | N/A | Active | 4 | 2 | 7
Propulsion Systems (Green Alt. Propellant) | 5 months | 4U | 0.7 kg | 10 W | Active | 4 | 3 | 9
Laser Beam | 18 years | 12U (est.) | 900 kg | 100 KW | Active | 5 | 5 | 1 (est.)
Ion-Beam​ | 700km to 500 km in 150 days | 12U (est.) | 5 kg | 3.3kW | Active | 5 | 5 | 1 (est.)

## Slide 24: How an Electrodynamic Tether works
End Mass
= Lorentz Force
= Magnetic Field
Flight Direction
Lorentz + Drag Force

## Slide 25: Stowed and Deployed Tether
End Mass
Electrodynamic Tether in Accordion Fold
100 m
26 mm
180 mm
200 mm

## Slide 26: Tether easily meets 25-year deorbit requirement
Chart: Altitude vs. Time
16.2 years
8.2 years
3 years
- - - - - - - - - - - - - - - - - - - - - -
25-year requirement

## Slide 27: Agenda
Introduction/Background Emily
System Engineering/Overview Maya
Debris Capture System James
Spacecraft Victor
Deorbit System Gustavo
Propulsion System Jasmine
Conclusion Emily

## Slide 28: Propulsion System
28
RPO movement
RPO movement
Propulsion System Functions:
Major Delta-V (Used for Large Altitude Changes)
Rendezvous Proximity Operations and Docking (RPOD) (Used for Capture)
Pitch Motion along y-axis
Translational Motion along z-axis
Major Delta-V

## Slide 29: Hybrid Design: Cold Gas and Green Propellant
Modified MarCo MiPS
Control Unit w/ Propellant Tank
ECAPS
1N HPGP Thruster
Green Propellant: ECAPS (Major Delta V)
29
ECAPS
Propellant Tank
Modified MarCo MiPS
12 RCS 25mN thrusters
Cold Gas: Modified MarCo MiPS (RPOD)

## Slide 30: Propulsion System Schematics
30
RPO movement
RPO movement
ECAPS Propulsion Schematic
Modified MarCo MiPS Propulsion Schematic

## Slide 31: Agenda
Introduction/Background Emily
System Engineering/Overview Maya
Debris Capture System James
Spacecraft Victor
Deorbit System Gustavo
Propulsion System Jasmine
Conclusion Emily

## Slide 32: Conclusion
Designed a 12U SmallSat that meets almost all project requirements.
Gained exposure to design and simulation tools
  MSC Adams
  SolidWorks
  Simscape
Coordinated as a remote team to deliver a project.

## Slide 34: Appendix

## Slide 35: Original Design Spun on Impact
Maximum Slew Rate
For these cases, 0.04 m/s (0.89 mph) is maximum relative velocity between debris and CubeSat
0cm
5cm
10cm
15cm
20cm

## Slide 36: Spin Reduction Options
Option | Active or Passive? | Mass | Volume | Initial Relative Velocities Enabled | Cons
Weighted Boom | Passive | 1.15 kg | 0.2 U | 5.3m/s (11.9mph) | Could fail through snapping
Reaction Wheels | Active | 1.7 kg | 1.2U | 5.1m/s (11.4 mph) | Requires added sensors, use of propulsion system
Propulsion | Active | 0.2kg | 0.2U | 5m/s (11.2 mph) | Requires added sensors
Notes: Reaction wheel from here: http://oak-aero.com/userfiles/1167/images/NewSpace-Systems/NewSpace-DS-Reaction-Wheel-1.pdf
Actually 1.55kg and 1U, but that’s for a one direction reaction wheel, would need to add gyroscope, sensors
Sensors: https://www.cubesatshop.com/product/nss-magnetometer/ + small boom estimate
Magnetometers would require estimating location and magnetic field, adding layer of complexity and opportunity for failure since it’s an active system

## Slide 37: A weighted boom reduces spinning
Now 5.3 m/s (11.9 mph) is maximum relative velocity between debris and CubeSat
Maximum Slew Rate
CubeSat
10m Boom
1kg Weight

## Slide 38: Boom Design
Carbon fiber collapsible tube mast design
Undeployed: 7.5cm*4cm*5cm = 0.15U
Deployed: 10m long
Weight: 150g
Collapsible Tube Mast Boom Design (Firth, MUSE Mechanism)